## Slide 1: Floating Point Addition and Subtraction

## Slide 2: Floating Point Addition Decimal first
9.999 × 101
+ 1.610 × 10–1
1. Align decimal points
  9.999 × 101
  + 0.016 × 101
2. Add significands
  9.999 × 101
  + 0.016 × 101
  = 10.015 × 101
3. Normalize result & check for over/underflow
  1.0015 × 102
4. Round and renormalize if necessary (assuming that you do not enough digits to represent)
  1.002 × 102

## Slide 3: Floating Point Addition (Binary)
  1.0002 × 2–1 0.5
  + –1.1102 × 2–2 + –0.4375
1. Align binary points
  Shift right number with smaller exponent (shift right 1.110)
  1.0002 × 2–1
  + –0.1112 × 2–1
2. Add significands (the second number is negative; we need to use 2’s complement to add)
01.000 × 2–1
+ 11.001 × 2–1 (‘sign’ bit added)
= 00.001 × 2-1
3. Normalize result & check for over/underflow
Overflow only if exponent is too large
Underflow if the fraction is zero
  1.0002 × 2–4, with no over/underflow

## Slide 4: Floating-Point Addition (Binary)
3.29 from textbook: Add 2.6125 *101 and 4.15039025 *10-1
First convert the numbers into binary
A = 2.6125 *101 = 26.125ten
= 011010.001 = 1.1010001 * 24binary
Exponent = 4, Biased = 127 + 4 = 131 = 1000 0011
A = 0 1000 0011 101 0001 0000 0000 0000 0000
= 0100 0001 1101 0001 0000 0000 0000 0000
= 0x41D10000

## Slide 5: Floating-Point Addition (Binary)
First convert the numbers into binary
B = 4.15039025 *10-1 = 0.415039025ten
  = 0.01101010001 = 1.101 0100 01 * 2-2
Exponent = -2; biased = 127 + -2 = 125 = 0111 1101
B = 0 0111 1101 101 0100 0100 0000 0000 0000
= 0011 1110 1101 0100 0100 0000 0000 0000
= 0x3ED44000

## Slide 6: Floating-Point Addition (Binary)
3.29 Add
A = 0 1000 0011 101 0001 0000 0000 0000 0000
B = 0 0111 1101 101 0100 0100 0000 0000 0000
Step 1: Subtract exponents (compare)
1000 0011 - 0111 1101 = 0000 0110 (6ten)
Exponent of B is smaller. Shift B’s significand (fraction) right by 6 positions
remember there is a hidden 1 in the fraction
shift right 1.
101 0100 0100 0000 0000 0000
= 0000 0110 1010 0010 0000 0000

## Slide 7: Floating-Point Addition (Binary)
Step 2: Add fractions
1. 1010 0010 0000 0000 0000 0000
+ 0. 0000 0110 1010 0010 0000 0000
= 1. 1010 1000 1010 0010 0000 0000
Step 3: Normalize-- already normalized (the exponent is the same as that of A)
= 0 1000 0011 101 0100 0101 0001 0000 0000

## Slide 8: Floating-Point Addition (IEEE format)
Let us work on another example
-11.5
+ 0.28125
A = -11.5
11.5 becomes 1011.12  normalized becomes 1.0111 *23
biased exponent = 3+127 = 1000 0010
Sign bit = 1. A = 1 1000 0010 011 1000 0000 0000 0000 0000
B = 0.28125 = 0.010012  normalize, becomes 1.001 *2-2
To represent in single precision, biased exponent = -2 + 127 = 125 = 0111 1101
Sign bit =0; B = 0 0111 1101 001 0000 0000 0000 0000 0000

## Slide 9: Floating-Point Addition (IEEE format)
To add A+B or Add
A = 1 1000 0010 011 1000 0000 0000 0000 0000
B = 0 0111 1101 001 0000 0000 0000 0000 0000
Step1: Subtract Exponents of A and B (remember subtraction requires 2’s complement
  A’s exponent = 1000 0010 - B’s exponent = 0111 1101 = 0000 0101 = 5ten
B’s exponent is smaller. So we need to shift B’s fraction right by 5 positions
Step 2: don’t forget hidden 1
Shift right 1.001 0000 0000 0000 0000 0000  0.0000 1001 0000 0000 0000 0000 0000

## Slide 10: Floating-Point Addition (IEEE format)
Step 3a: A’s fraction = 1. 011 1000 0000 0000 0000 0000
Before we add these two fractions of A and B, note A is negative.
So we need to get 2’s complement of A’s fraction (add one extra bit on the left for sign)
2’s complement of 01. 011 1000 0000 0000 0000 0000
10.100 1000 0000 0000 0000 0000

## Slide 11: Floating-Point Addition (IEEE format)
Step 3b: Add fractions
10.10010000000
+ 00.00001001000
= 10.10011001000  result is negative (2’ complement)
convert fraction to positive value (magnitude)  take 2’s complement
= 01.01100111000  can drop sign bit now

## Slide 12: Floating-Point Addition (IEEE format)
Step4: Normalize
= 1.011 0011 1000 0000 0000 0000  result is already normalized
the fraction part we will use = 011 0011 1000 0000 0000 0000
Exponent of Result (same as that A) = 1000 0010
Step 5: Sign of result is negative.
Final result = 1 1000 0010 011 0011 1000 0000 0000 0000
If you are curious about correctness.
Fraction 1.011 0011 1000 0000 0000 0000*23 = 1011. 0011 1000 0002 = 11.21875ten
Sign is negative. So the result is -11.21875  -11.5 +0.28125ten

## Slide 13
For example (0.5 - 0.375) or
A= 0.5 = 0.1 or 1.0 *2-1 Biased exponent = -1+127 = 126 = 0111 1110
A = 0 0111 1110 000 0000 0000 0000 0000 0000
B = 0.375 = 0.011 = 1.1 *2-2 Biased exponent = -2+127 = 125 = 0111 1101
B = 0 0111 1101 100 0000 0000 0000 0000 0000
Likewise, if we are performing subtraction, we need to complement subtrahend
And then add fractions.
NOTE: Fractions of negative numbers are NOT in 2’s complement
When we added 1.0002 × 2–1 + –1.1102 × 2–2 (0.5 + –0.4375)decimal
Shift number with smaller exponent (shift left 1.110)
1.0002 × 2–1 + –0.1112 × 2–1
We complemented the negative number to perform addition of fractions
Floating Point Subtraction

## Slide 14
Subtract A = 0 0111 1110 000 0000 0000 0000 0000 0000
B = 0 0111 1101 100 0000 0000 0000 0000 0000
Step 1: Subtract Exponents: (126-125) = 1
Step 2: Shift the fraction of the smaller exponent (B) right by one position
remember the implied 1 in the fraction
B’s fraction: = 0.110 0000 0000 0000 0000 0000
Step 3a: Need to get 2’s complement of subtrahend (B) = 11.010 0000 0000 0000 0000 0000
I am using an additional bit on the left to represent sign
Step 3: Add the fractions A= 01.000 0000 0000 0000 0000 0000 *2-1
B = 11. 010 0000 0000 0000 0000 0000 *2-1
= 00. 010 0000 0000 0000 0000 0000 *2-1
= 0.025ten
Floating Point Subtraction

## Slide 15
Result needs to be normalized
Step 4: Normalize fraction if necessary (and adjust exponent)
Result = 00. 010 0000 0000 0000 0000 0000 = 1.000 0000 0000 0000 0000 0000 *2-3
the exponent before normalization is -1
and we needed shift decimal point left by 2 position
hence the new exponent is (-1 -2) = -3
Biased exponent = -3+127 = 124 = 0111 1100
Step 5: So, result is 0 0111 1100 000 0000 0000 0000 0000 0000
Floating Point Subtraction

## Slide 16
What happens if result is negative (either for addition or subtraction operations)?
We saw this happen when we performed -11.5 +0.28125ten
Fraction of the Result would be in 2’s complement
--> but we only represent actual value, not in 2’s complement
First take 2’s complement of the result fraction, normalize
Find exponent and fraction representations
But the sign bit will be 1
Try some examples on your own
Floating Point Subtraction