## Slide 1: The Processor
Sections you should read
4.1 Introduction
4.2 Logic Design Conventions
4.3 Building a Datapath
4.4 A Simple Implementation Scheme
4.5 An Overview of Pipelining
4.6 Pipelined Datapath and Control
4.7 Data Hazards: Forwarding versus Stalling
4.8 Control Hazards
4.9 Exceptions

## Slide 2
Application geography
All program code  machine language code (.text part) is stored in memory
All program data (.data part) for the program is also stored in memory
Processor cannot tell the difference between data and instructions
A 32-bit data can be viewed as an instruction (that is as Opcode and operands)
Chapter 4: The Processor
For example 1100 1011 0000 1001 0000 0001 0100 1011
Represents: SUB X11, X10, X9
11001011000 01001 000000 01010 01011
As an integer number (signed/un) -888,602,293 3,406,365,003
a single precision floating point number -8,978,763.00000

## Slide 3
Chapter 4: The Processor
For example 1100 1011 0000 1001 0000 0001 0100 1011
or
a negative integer: -888,602,293ten
2’s complement = 0011 0100 1111 0110 1111 1110 1011 0101
1100 1011 0000 1001 0000 0001 0100 1011
Or a floating point number: 1 1001 0110 000 1001 0000 0001 0100 1011
exponent = +22 and fraction = 1. 000 1001 0000 0001 0100 1011 approx -1.07035 *223
This is how most security attacks take place  make processor execute data as instructions

## Slide 4
Remember how (virtual) memory space is used to store different parts of your programs
Chapter 4: The Processor
Modern OS will make sure that PC’s can only be loaded with text segment addresses
If PC address falls outside of defined text segment, programs are stopped

## Slide 5
How is an instruction executed?
Chapter 4: The Processor
Step 1: fetch instruction from (instruction) memory
The address of the instruction is in Program Counter (or PC)
Read memory using PC as an address
Increment PC by 4 so that it points to the next instruction
Step 2: decode the instruction: examine the 32-bit instruction, understand opcode
if operands are in registers, read source registers
ADD X2, X3, X4 or LDUR X2, [X27, #0]
CBNZ X1, X2, label
if the operator will be acting on an immediate value or an address
the sign of the number needs to be extended to 64 bits
ADDI X2, X3, #-22 B Exit
B.LE Loop CBZ X4, NextRecord

## Slide 6
Step 3-Branch: execute the instruction
If conditional branch? Example: B.LT loop
we still need ALU to compare (or subtract registers)
if the condition is true, change PC value to the address of loop
If the next instruction to be executed is a branch to an address of loop
if condition is false, (PC is already incremented by 4 )
and execute next instruction in sequence
If condition is true. Add instruction offset to the PC and skip steps 4 and 5
If BL, first save PC in X30 and then change PC to function address
Chapter 4: The Processor
Step 3-Logic: execute the instruction
if arithmetic, perform arithmetic operation
ADD, SUB, MUL, DIV, ORR, …

## Slide 7
Step 4: Access memory to read or write
if load: Get data from memory
LDUR X2, [X0, #0]
if store, store value of the register into memory
STUR X2, [X0, #0]
Chapter 4: The Processor
Step 5: store result to register
if arithmetic, store the result of ALU into destination register
ADD X2, X3, X4
if load, load value of the register into memory
LDUR X2, [X0, #0]

## Slide 8
Information encoded in binary
  Low voltage = 0, High voltage = 1
  Bus: nothing but a collection of wires to transmit data
    One wire per bit
    Multi-bit data encoded on multi-wire buses
Logic Design Basics
Combinational element (does not use clocks, takes as long as it takes)
  Operate on data and perform Boolean logic
  Output is a function of input
  Timing is based on the slowest operation (multiply or square root)
State (sequential) elements (require clock, coordination matters)
  Store new information based
    Current information
    Computations performed by combinational logic
       when clock signal arrives

## Slide 9
Combinational Elements
AND-gate
Y = A & B
I0
I1
Y
M u x
S(ignal)
Multiplexer
Y = either I0 or I1
A
B
Y
+
Arithmetic/Logic Unit
Y = F(A, B)
A
B
Y
ALU
F
Adder
Y = A + B

## Slide 10
Combinational logic transforms data during clock cycles (add, sub shift,…)
  Computes the inputs to the sequential circuits
  May depend on the current “state” or values stored in sequential circuits (flip flops)
    Sequential circuits are wires holding a charge (0 or 1)
  May also use additional information for computing next inputs to flip flops
  Computation takes place Between clock edges
Clocking Methodology

## Slide 11
Datapath
  Elements that process data and addresses and connections between them Registers, ALUs, mux’s, combinational circuits, memories,
Building a Datapath

## Slide 14
Datapath
  Elements that process data and addresses and connections between them Registers, ALUs, mux’s, combinational circuits, memories, …
We will build an ARMv8 (or LEGv8) datapath incrementally
  Remember the steps involved in the execution of instructions
  Fetch instruction,
  Decode instruction, fetch register operands,
  Execute ALU operation
  Access memory for load/store, update PC for branch instructions
  Store results in destination register
Building a Datapath
Let us first review the binary representations of instructions we studied in Chapter 2

## Slide 15
(R-type) Register Instruction
opcode
Rm
shamt
Rn
Rd
11 bits
5 bits
6 bits
5 bits
5 bits
R-Type
An example ADD X0, X9, X10
In binary, we have opcode, source, source, destination
10001011000
01010
000000
01001
00000
Opcode (ADD)
Rm= X10
shmt
Rn=X9
Rd=X0

## Slide 16
Step 1: Instruction Fetch
64-bit register
Increment by 4 for next instruction
Use PC as address to memory and read the instruction from (instruction) memory
Increment PC by 4 (instructions are 32 bits or 4 bytes long)
This part is the same for any instruction
While an instruction is executing, PC points to next instruction

## Slide 17
Step 2: Decode and register fetch for R-Format Instructions

## Slide 18
Read two register operands
Perform arithmetic/logical operation
Write register result
Step 2: Decode and register fetch for R-Format Instructions
ADD X4, X5, X6
opcode
Rm X6
shamt
Rn X5
Rd X4
11 bits
5 bits
6 bits
5 bits
5 bits
  opcode: operation code
  Rm: the second register source operand
  shamt: shift amount (00000 for now)
  Rn: the first register source operand
  Rd: the register destination

## Slide 19
Step 3: Instruction Execution: R-Format
We fetched the two source operands during decode
We now perform the actual operation (ADD, SUB,….)

## Slide 20
Not needed for an R-type instruction
Step 4: Memory

## Slide 21
Step 5 – Write Back
Step 4: Write Results Back

## Slide 22
(D-type) Data Instruction
D-Type
Load/store instructions
  Rn: base register (or Index register)
  address: constant offset from contents of base register (+/- 32 double words)
  Rt: destination (load) or source (store) register number
For example: LDUR X2, [X1, #8]
11111000010 000001000 00 00001 00010
opcode
op2
Rn
Rt
11 bits
9 bits
2 bits
5 bits
5 bits
address

## Slide 23
Step 1: Instruction Fetch
64-bit register
Increment by 4 for next instruction
Use PC as address to memory and read the instruction from (instruction) memory
Increment PC by 4 (instructions are 32 bits or 4 bytes long)
This part is the same for any instruction
While an instruction is executing, PC points to next instruction

## Slide 24
Read register operands
Calculate address using 9-bit offset
  Use ALU, but sign-extend offset
Load: Read memory and update register
Store: Write register value to memory
Step 2: Decode and register fetch for D-Format Instructions
LDUR X3, [X19, #16]
opcode
op2
Rn X19
Rt
11 bits
9 bits
2 bits
5 bits
5 bits
Address. 16
  Rn: base register
  address: constant offset from contents of base register (+/- 32 double words)
  Rt: destination (load) or source (store) register number
Register
Registers
Instruction
Sign-Extend
9
64

## Slide 25
Step 3: Execution
EX: LDUR X2, [X27, #8]
During decode we fetched the base address register (X27), computed sign extended constant (8)
Now we add the base and the offset to get the memory address
opcode
op2
Rn
Rt
11 bits
9 bits
2 bits
5 bits
5 bits
address
Register read
Sign extended constant

## Slide 26
Step 4: Memory: Read or Write
EX: LDUR X2, [X27, #8]
During decode we fetched the base address register (X27), computed sign extended constant (8)
opcode
op2
Rn
Rt
11 bits
9 bits
2 bits
5 bits
5 bits
address
Now we retrieve from or store to memory
We send the address to memory and wait until we get the data back from memory
Register read
Sign extended constant

## Slide 27
Step 5 – Write Back
Step 4: Write Results Back

## Slide 28
CBZ Xi, L1 //if (Xi == 0) branch to instruction labeled L1;
CBNZ Xi, L1 //if (Xi != 0) branch to instruction labeled L1;
B L1 //branch unconditionally to instruction labeled L1;
Instruction Formats
(B-type) Branch Operations
000101
16ten (Address of Label)
6 bits
26 bits
Unconditional Branch instructions: B L1
1011 0101
L1 (distance from current instruction)
8 bits
19 bits
19
5 bits
Conditional Branch: CBNZ X19, L1

## Slide 29
Step 1: Instruction Fetch
64-bit register
Increment by 4 for next instruction
Use PC as address to memory and read the instruction from (instruction) memory
Increment PC by 4 (instructions are 32 bits or 4 bytes long)
This part is the same for any instruction
While an instruction is executing, PC points to next instruction

## Slide 30
What are the different types of branch instructions
CBZ reg, label // if (reg) = 0, branch to label
CBNZ reg, label
We need to read the register and the label
Step 2: Decode and register fetch for Branch-Format Instructions
Register
Registers
Instruction
Sign-Extend
16
32
Need to compare with zero
Need to add to PC
opcode
Relative distance
Rn
11 bits
5 bits
16 bits
  Rn: operand to compare with zero
  Relative Distance: this value will be added to PC to find address to branch

## Slide 31
Step 3: Execution: Branch
EX: B.LT loop
opcode
Relative distance
Cond
11 bits
3 bits
19 bits
Why Shift Left by 2 (multiply by 4)?

## Slide 32
Step 4 and 5: Memory and Write Back
Not needed for a Branch Instruction

## Slide 33
Full Datapath

## Slide 34
Defining control path
We need to design circuits that trigger transfer of data among the different units in the data path.
When do we read 2 register operands (R type and STUR)
When do we read 1 register operand (LD/STUR, Conditional Branch, Immediate
When do we NOT read any register operands (B, BL)
Likewise, are we asking the ALU to perform ADD, SUB,….
Are we asking data memory to read data from memory (LDUR)
or store data into memory (STUR)
So these “decisions” control what data flows from one unit to another
and what actions are taken
Most of this information comes from Opcode itself

## Slide 35
Defining control path
Everything in Blue is part of the control path

## Slide 36: Instructions and ALU inputs

## Slide 37
ALU used for
  Load/Store (LDUR or STUR) –need to add base register + constant
    So, ALU performs ADD
  Conditional Branch: Need to compare two registers
    So, ALU performs SUB
  R-type: ALU performs the operation depending on the OPCODE
ALU Operation control
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | pass input b
1100 | NOR
Our ALU takes 4 bit control
And performs an operation on its inputs

## Slide 38
Now, let us see how OPCODE is used to control other parts of the datapaths
Different number of opcodes for different instructions
The Main Control Unit

## Slide 39: Instruction Formats

## Slide 40
Datapath with Control - START
Sign extend should take
9, 16, 19 or 26 bits and extend
to 32 bits or 64 bits
For R instructions, the second source register number is in bits 20-16
For CB and STUR the 2nd register is in bits 4-0
For CB this is the compare reg
For STUR this is the value to be stored in memory
 This is the position of destination reg for most other instructions (R and LDUR)

## Slide 41
Datapath With Control
Datapath With Control
opcode
Rm
shamt
Rn
Rd
31-21
(11 bits)
20-16
(5 bits)
15-10
(6-bits)
9-5
(5-bits)
4-0
(5-bits)
R-Type
D-Type
LDUR
opcode
op2
Rn
Rd
31-21
(11 bits)
20-12
(9 bits)
11-10
(2 bits)
9-5
(5 bits)
4-0
(5 bits)
address
D-Type
STUR
opcode
op2
Rn
Rm
31-21
(11 bits)
20-12
(9 bits)
11-10
(2 bits)
9-5
(5 bits)
4-0
(5 bits)
address
Rn is the register containing base address,
Rm the register value that will be stored in memory

## Slide 42
Datapath With Control
Let us try to understand the various control signals derived from Opcode
Let us consider which bits specify the register operands.
Their bit positions vary from instruction to instruction.
opcode
Rm
shamt
Rn
Rd
11 bits
5 bits
6 bits
5 bits
5 bits
For R type, the TWO source registers are Rm (bits 16-20) and Rn (bits 5-9)
Remember, we get different number bits for sign extend (9, 16, 19 or 26)

## Slide 43
Datapath With Control
Let us try to understand the various control signals derived from Opcode
Let us consider which bits specify the register operands.
Their bit positions vary from instruction to instruction.
opcode
op2
Rn
Rt
11 bits
9 bits
2 bits
5 bits
5 bits
address
For LDUR and STUR, the base address which is a source register is Rn (bits 5-9)
For STUR, the second source (data to store in memory) is Rt (bits 0-4). This is the destination register for LDUR
Remember, we get different number bits for sign extend (9, 16, 19 or 26)

## Slide 44
Datapath With Control
Let us try to understand the various control signals derived from Opcode
Let us consider which bits specify the register operands.
Their bit positions vary from instruction to instruction.
opcode
Relative distance
Rn
11 bits
5 bits
16 bits
For CBZ (and CBNZ), the source register is Rn (bits 0-4)
Remember, we get different number bits for sign extend (9, 16, 19 or 26)

## Slide 45
Datapath With Control
The bit = 0
The bit = 1
Let us try to understand the various control signals derived from Opcode

## Slide 46
Datapath With Control
We will now see how different instructions (opcodes) produce either a 0 or 1 for each of the control signals
Consider R-format signals
Reg2Loc
0  the 2nd src reg is in bits 20-16
ALUSrc
0  the two inputs to ALU are registers
MemtoReg
0  result from ALU is stored in dest reg
RegWrite
1  We will write a value to dest reg
MemRead
0  we will not read from memory
MemWrite
0  we will not write to memory
Branch
0  not a branch instruction
ALUop
1,0 = 10  ALU op depends on Opcode

## Slide 47
R-Type Instruction
Note the datapaths enabled in this case.
Instruction Fetch
Read TWO registers
Perform ALU operation
Store result in destination register

## Slide 48
Tracing Datapath Ex: ADD X0, X1, X2
10001011000
X2
xxxxx
X1
X0

## Slide 49
Tracing Datapath Ex: SUBI X0, X1, #2
1101 0001 00 00 0000 0000 10 00 001 0 0000

## Slide 50
Note the datapaths enabled in this case.
Instruction Fetch
Read ONE register
Add register+constant to get memory address
Read data from memory
Store data into dest register
Load Instruction

## Slide 51
Tracing Datapath Ex: LDUR X0, [X1, #8]

## Slide 52
Note the datapaths enabled
Instruction Fetch
Read Two registers
one contains address
second contains data to store
Reg2Loc = 1
Add register+constant to get memory address
  ALUSrc = 1
Store data into memory
  RegWrite = 0
  MemRead = 0, MemWrite = 1
ALU Control input 00
ALU Control output 0010
Store: STUR X0, [X1, #8]

## Slide 53
Consider conditional branches
Two types:
CBZ X5, label or CBNZ X5, label
 check if a register (X5) is zero or not zero

## Slide 54
Consider conditional branches
The second type checks condition code bits N, Z, OV, C
SUBS XZR, X1, X2 // set condition code bits
B.LE label // branch if either N or Z are set
What do we need in the datapath to implement this type of branch?
Our ALU must have condition code bits and set them when SUBS is executed
We need additional gates that check if specific bits of CC are set

## Slide 55
Consider conditional branches
ALU must contain CC register
Set these bits (N, Z, OV, C)
Be able to check which bit is set
As well as combination of bits
(LE  N OR Z
GE  (not) N OR Z

## Slide 56
Note the datapaths enabled in this case.
Instruction Fetch
Read ONE register
Compare to Zero
If true, add “constant” to PC and change PC
CBZ Instruction

## Slide 57
Tracing Datapath Ex: CBZ X0, L1

## Slide 58
Implementing Unconditional Branch
Unlike CBZ, we do not add the address/constant to PC
   the address specified in bits 25-0 is the address of branch (not relative to PC)
Update PC with concatenation of
  Top 4 bits of old PC
  26-bit jump address
  00 (to get byte address from word address (shift left by 2 positions)
Need an extra control signal decoded from opcode
2
address
31:26
25:0
31-28
(no change)
27-2
00
New PC contents

## Slide 59
Datapath With Branch (B) Added
Note, this Adder is NOT used for unconditional branches.
The sign extended 26 bits from the instruction are shifted left two places, and stored in bits 0-27 of PC

## Slide 60
Tracing Datapath Ex: B L1

## Slide 61
Assume 2-bit ALUOp derived from opcode
  Combinational logic drives ALU control
ALU Control
opcode | ALUOp | Operation | Opcode field | ALU function | ALU control
LDUR | 00 | load register |  | add | 0010
STUR | 00 | store register |  | add | 0010
CBZ | 01 | compare and branch on zero |  | pass input b | 0111
R-type | 10 | add | 100000 | add | 0010
 |  | subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | ORR | 100101 | OR | 0001

## Slide 62
Possible Quiz Problems – R Type Instr
AND instruction: AND Rd, Rn, Rm
opcode
Rm
shamt
Rn
Rd
11 bits
5 bits
6 bits
5 bits
5 bits
What are the control signals generated by this line of code
Reg2Loc =
ALUSrc =
ALU Op =
ALU Control =
MemRead =
MemWrite =
MemToReg =
RegWrite =
0
0
10
0000
0
0
0
1

## Slide 63
Possible Quiz Problems – D Type Instr
STUR Rt, [Rn, #66]
opcode
Dt Adrs
Op
Rn
Rt
12 bits
31 21
9 bits
20 12
2 bits
11 10
5 bits
9 5
5 bits
4 0
What are the control signals generated by this line of code
Reg2Loc =
ALUSrc =
ALU Op =
ALU Control =
MemRead =
MemWrite =
MemToReg =
RegWrite =
1
1
00
0010
0
1
X
0

## Slide 64: Control Flags
 | Reg2Loc | ALUSrc | ALUOp | ALU Control | Branch | MemRead | MemWrite | MemToReg | RegWrite | Type
ADD | O | O | 1O | OO1O | O | O | O | O | 1 | R
ADDI | X | 1 | 11 | OO1O | O | O | O | O | 1 | I
AND | O | O | 1O | OOOO | O | O | O | O | 1 | R
ANDI | X | 1 | 11 | OOOO | O | O | O | O | 1 | I
CBZ | 1 | O | O1 | O111 | 1 | O | O | X | O | CB
LDUR | X | 1 | OO | OO1O | O | 1 | O | 1 | 1 | D
ORR | O | O | 1O | OOO1 | O | O | O | O | 1 | R
ORRI | X | 1 | 11 | OOO1 | O | O | O | O | 1 | I
STUR | 1 | 1 | OO | OO1O | X | O | 1 | X | O | D
SUB | O | O | 1O | O11O | O | O | O | O | 1 | R
SUBI | X | 1 | 11 | O11O | O | O | O | O | 1 | I

## Slide 65: control signals

## Slide 66: AND X3, X1, X2
Reg2Loc = 0 X2
ALUSrc = 0
ALU Op = 10
ALU Control = 0000
MemRead = 0
MemWrite = 0
MemToReg = 0
RegWrite = 1 X3
A X1
B X2
C ___
D X2
E 0000

## Slide 67: ADD X0, X1, X2
Reg2Loc = 0 X2
ALUSrc = 0
ALU Op = 10
ALU Control = 0010 MemRead = 0
MemWrite = 0
MemToReg = 0
RegWrite = 1 X0
A X1
B X2
C ___
D X2
E 0010

## Slide 68: ADDI X1, X2, #42
Reg2Loc = X
ALUSrc = 1
ALU Op = 11
ALU Control = 0010
MemRead = 0
MemWrite = 0
MemToReg = 0
RegWrite = 1
A X2
B ___
C ___
D #42
E 0010

## Slide 69: STUR X1, [X2, #42]
Reg2Loc = 1
ALUSrc = 1
ALU Op = 00
ALU Control = 0010
MemRead = 0
MemWrite = 1
MemToReg = 0 (X)
RegWrite = 0
A X2
B ___
C ___
D #42
E 0010

## Slide 70
Some problems from Textbook
4.3. Consider the following instruction mix
R-type | I-type | LDUR | STUR | CBZ
24% | 28% | 25% | 10% | 11%
4.3.1. What fraction of instructions use data memory
LDUR + STUR = 35%
4.3.2. What fraction of instructions use instruction memory
ALL instructions = 100% (need to fetch instruction from Instr Memory)
4.3.3. What fraction of instructions use sign-extend unit
I-type, LDUR, STUR, and CBZ = 74%
4.3.4 What is sign-extend unit doing when its output is not needed
It still does sign extend, but the output is not selected by the mux.