## Slide 1
Chapter 3
This chapter deals with Computer Arithmetic
Integer Addition and Integer Subtraction (using complement addition)
Integer Multiplication
Integer Division
Floating point: Single and Double precision representations
Representing positive and negative floating-point numbers
Floating point Addition (and subtraction)
Floating point Multiplication and Division

## Slide 2
Chapter 3
Signed and unsigned integers
negative numbers use 2’s complement
We use 2’s complement addition to subtract numbers
A= 10ten 0 1010
B = 5ten 0 0101 - B = 11011
A-B = A + (-B) 0 1010 + 1 1011 = 0 101 = 5ten
This chapter deals with Computer Arithmetic
Integer Addition and Integer Subtraction (using complement addition)
Integer Multiplication
Integer Division
Floating point: Single and Double precision representations
Representing positive and negative floating point numbers
Floating point Addition (and subtraction)
Floating point Multiplication and Division

## Slide 3
Addition
More general ALU
ALU
A
B
m
ovf
S
64
64
64
Control (opcode)
c
When can we get an overflow during addition or subtraction?
If the result is “too large”
Add two positive numbers and result is negative
Subtract one negative number from another and result is positive
Operation | Operand A | Operand B | Result indicating overflow
A + B | ≥ 0 | ≥ 0 | < 0
A + B | < 0 | < 0 | ≥ 0
A – B | ≥ 0 | < 0 | < 0
A – B | < 0 | ≥ 0 | ≥ 0

## Slide 4
Signed and Unsigned numbers
Signed  both positive and negative numbers
  Negative numbers are represented as 2’s complement
    Complement bits and add 1
  Complement means 1 → 0, 0 → 1
Example: negate +2
  +2 = 0000 0000 … 00102
  –2 = 1111 1111 … 11012 + 1 = 1111 1111 … 11102
Now lets us consider what happens when we want to take a 32 bit number and store that in a 64 bit register
Should the remaining 32 bits be zeros?
If unscaled/unsigned YES (we are treating 32 bit original number as unsigned)
If the original number is signed – we copy sign bit for the remaining 32 bits WHY?
Sign Extended

## Slide 5
Base 16
  Compact representation of bit strings
  4 bits per hex digit or 2 digits per byte
Example: eca8 6420 (8 hex digits, 4 byte or 32 bits)
  1110 1100 1010 1000 0110 0100 0010 0000
You need to get comfortable converting Hex into binary and binary to Hex
Hexadecimal (Hex) numbers
0 | 0000 | 4 | 0100 | 8 | 1000 | c | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | d | 1101
2 | 0010 | 6 | 0110 | a | 1010 | e | 1110
3 | 0011 | 7 | 0111 | b | 1011 | f | 1111

## Slide 6
Signed and unsigned integers
negative numbers use 2’s complement
We use 2’s complement addition to subtract
A= 10ten 0 1010
B = 5ten 0 0101 - B = 11011
A-B = A + (-B) 0 1010 + 1 1011 = 0 101 = 5ten
Another Example
A= 5ED4hex = 0101 1110 1101 0100binary
B = 07A4hex = 0000 0111 1010 0100binary
Compute A- B in binary
2’s complement of B (that is we need –B)
-B = 1111 1000 0101 1100
A = 0101 1110 1101 0100
+ = 0101 0111 0011 0000
How to convert decimal to binary
Divide by 2 repeatedly
= 105/2 = 52, R=1
52/2 = 26, R=0
26/2 = 13, R=0
13/2 = 6, R=1
6/2 = 3, R=0
3/2 = 1, R=1
1/2. = 0, R=1
10510 = 11010012
Chapter 3