## Slide 1
Pipelined laundry: overlapping execution  4 tasks: Wash, Dry, Fold, Put away
  Parallelism improves performance
Single cycle instructions vs pipelined
One at a time
  Throughput = loads * stages * time = 4 x 4 x .5 = 4 loads per 8 hrs
Non-stop
  Speedup = (loads + (stages - 1)) * time = ( 4 + ( 4 - 1)) * .5 = 4 loads per 3.5 hrs

## Slide 2
We can consider instruction execution as a 5-part task
  IF: Fetch instruction from instruction memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
    CBZ/CBNZ use ALU (to subtract) and then update PC
    ALU operations are completed in this task
    LDUR/STUR Memory address is computed in this stage
  Data Access: Access memory operand
  LDUR read data from memory
  STUR store data into memory
  Other instructions do not do anything in this task
  WB: Write result back to register
  Not used by branch/conditional branch and STUR
  write result into destination Register – LDUR, ADD, SUB, ORR, AND
Pipeline

## Slide 3
Pipeline Design
We have several instructions going through our datapaths simultaneously.
In each cycle:
1. a new instruction is being fetched
2. an instruction which (already fetched) is decoded and register values are read
3. an instruction which (input registers are already read) may be using ALU either to perform arithmetic operation for R-type or to add (Rbase)+offset to obtain address for Load/Store
4. an instruction which (address already computed) may be accessing memory for load or store instructions (otherwise no action in this stage)
5. an instruction which (completed ALU or Load operation) is attempting to store results in Rd
We need to keep track of all these (5) instructions in our datapaths
The control paths also need to make sure that the control signals relate to correct instructions

## Slide 4
Assume time for different tasks are
  100ps for register read or write
  200ps for other tasks (ignore control and mux delays)
Compare pipelined datapath with single-cycle datapath
Pipeline Performance
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
LDUR | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
STUR | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
CBZ | 200ps | 100 ps | 200ps |  |  | 500ps
We need to use a clock that allows the slowest operation to complete

## Slide 5
Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)
Cycle time = time for longest instruction = 800ps
Cycle time = slowest pipeline stage
= 200ps
Speedup = 800/200 ~ 4
100ps wasted

## Slide 6
Pipelined laundry: overlapping execution  4 tasks: Wash, Dry, Fold, Put away
  Parallelism improves performance
Single cycle instructions vs pipelined
One after another
  Throughput = loads * stages * time = 10K x 4 x .5 = 20K = 10K loads per 20K hrs
Non-stop
  Speedup = (loads + (stages - 1)) * time = (10K+ ( 4 - 1)) x .5 = 10.003K loads per 5001.5 hrs

## Slide 7
Pipeline Performance
Let us consider how instructions flow through a pipeline
1: ADRP X0, v
2: ADD X0, X0, :lo12:v
3: LDUR X1, [X0, #0]
4: LDUR X2, [X0, #8]
5: ADD X1, X1, X2
6: LDUR X2, [X0, #16]
7: ADD X1, X1, X2
CYCLE | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ADRP X0, v | IF | ID | EX |  | WB |  |  |  |  |  |  | 
ADD X0, X0, :lo12:v |  | IF | ID | EX |  | WB |  |  |  |  |  | 
LDUR X1, [X0, #0] |  |  | IF | ID | EX | MEM | WB |  |  |  |  | 
LDUR X2, [X0, #8] |  |  |  | IF | ID | EX | MEM | WB |  |  |  | 
ADD X1, X1,X2 |  |  |  |  | IF | ID | EX |  | WB |  |  | 
LDUR X2, [X0, #16] |  |  |  |  |  | IF | ID | EX | MEM | WB |  | 
ADD X1, X1,X2 |  |  |  |  |  |  | IF | ID | EX |  | WB | 
STUR X1, [X0, #16] |  |  |  |  |  |  |  | IF | ID | EX | MEM | 

## Slide 8
Pipeline Datapaths (slightly modified)

## Slide 9
  To hold information produced in previous cycle (including control signals)
Need registers (or buffers) between stages

## Slide 10
Pipeline Datapaths
Tracks instruction fetched
Tracks instruction decoded
Tracks instruction completed EX
Tracks instruction completed EX or Mem

## Slide 11: Pipeline Datapaths Data passed between stages
IF/ID:
Instruction: Since the opcode is needed in decode and execute stages;
Operands: Needed in decode, execute and write back stages.
PC: Decode and execute stage since a branch instruction may change the flow
ID/EX:
Register operands values read in Decode to Execute stage;
Destination register number and Opcode for Execute, MEM or WB stage
Control signals generated using opcode to other stages
EX/MEM:
Result of ALU operation either for WB or memory access.
Destination register number and opcode for MEM and WB stages
MEM/WB:
ALU result or value read from memory to WB
Destination register number (and opcode to determine if WB needs to write a result or not

## Slide 16
State of the pipeline at clock cycle 5  snapshot of the pipeline stages on a specific clock cycle
Yet another view of pipeline
X13
#48
X1
X3
X4
(X2-X3)
[X1, 40]
X12
X11
X13
X10
[PC] ->
1OOO1O11OOO OO1O1 OOOOOO OO11O O111O

## Slide 17
State of the pipeline at clock cycle 5  snapshot of the pipeline stages on a specific clock cycle
Yet another view of pipeline
X6
#48
X5
X1
(X3+X4)
(X2-X3)
X14
X13
X14
X12
X11

## Slide 18
State of the pipeline at clock cycle 5  snapshot of the pipeline stages on a specific clock cycle
Yet another view of pipeline
X6
X5
X3+X4
X14
X13
X12
[X1, #48]

## Slide 19
State of the pipeline at clock cycle 5  snapshot of the pipeline stages on a specific clock cycle
Yet another view of pipeline
X5+X6
X14
X13
[X1, #48]

## Slide 20
State of the pipeline at clock cycle 5  snapshot of the pipeline stages on a specific clock cycle
Yet another view of pipeline
X5+X6
X14

## Slide 21: Limitations to pipeline performance
In the ideal case, with 5 stage pipeline (as we have seen) we should get 5 times the speedup compared to un-pipelined computer
because 5 instructions are being executed
But we do not always get this performance– Why?
Hazards
Situations that prevent starting next instruction in the next cycle
Structure hazards
  A required resource is busy (what if we only had one type of memory?)
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction
  For conditional branch – what is the next instruction to fetch?